## Slide 1
Prediction of Guidewire Crossing of CTO by Pre-Procedural Coronary CT Angiography
KCCT (Korean CTO CT multicenter registry) Score as a Tool for Assessing Difficulty in CTO PCI
2016-12-10, JCR, Busan, Korea
Jin-Ho Choi, Cheol-Woong Yu, Hyun-Jong Lee, Jon Suh, Nae-Hee Lee, Sang-Min Park
Samsung Medical Center, Sejong General Hospital, Korea University Anam Hospital, and Soonchunhyang University Bucheon Hospital

## Slide 2
Prediction of Guidewire Crossing of CTO by Pre-Procedural Coronary CT Angiography
KCCT (Korean CTO CT multicenter registry) Score as a Tool for Assessing Difficulty in CTO PCI
2016-07-21, TOPIC, Tokyo, Japan
Jin-Ho Choi, Cheol-Woong Yu, Hyun-Jong Lee, Jon Suh, Nae-Hee Lee
Samsung Medical Center, Sejong General Hospital, Korea University Anam Hospital, and Soonchunhyang University Bucheon Hospital

## Slide 3
Prediction of Guidewire Crossing of CTO by Pre-Procedural Coronary CT Angiography
KCCT (Korean CTO CT multicenter registry) Score as a Tool for Assessing Difficulty in CTO PCI
2016-06-18, CTO-Club, Nagoya, Japan
Jin-Ho Choi, Cheol-Woong Yu, Hyun-Jong Lee, Jon Suh, Nae-Hee Lee
Samsung Medical Center, Sejong General Hospital, Korea University Anam Hospital, and Soonchunhyang University Bucheon Hospital

## Slide 4: (Traditional) angiographic predictors of CTO PCI success
Unfavorable
Favorable
But, the prediction power is not high!

## Slide 5: How to utilize CT for CTO PCI
Before PCI, CT imaging tell us …
  Nature of CTO plaque (Choi JH, Circ J 2011)
  Physiology of CTO (Choi JH, Circ Img 2014; Choi JH, JACC Intv 2015)
  How to plan PCI procedure (case series)
  How to predict PCI procedural success
During PCI, imaging tell us …
  Right course of wire (with CT-angio hybrid system)

## Slide 6: Use of coronary CT for prediction of CTO PCI success
Potential anchor balloon site
Large ostium with horizontal position
No calcification
Straight CTO line
‘Island btw. CTO and distal STO
Distal exit target, distal vessel size (length and diameter), and side branch
‘Tapered’ entry site

## Slide 7: Methods
Retrospective multicenter registry
  Samsung Medical Center
  Sejong General Hospital
  Korea University Anam Hospital
  Soonchunhyang University Bucheon Hospital
Inclusion criteria
  Consecutive CTO PCI case with pre-procedural CT within 6 week, Jan 2007 ~ May 2015
Exclusion criteria
  AMI within 90 days by CT acquisition time
  Occlusion of bypass graft or small vessel (diameter < 2.0 mm)
  Inadequate imaging quality

## Slide 8: Data Analysis
Coronary CT angiography
  Dedicated workstation (Terarecon iNtuition)
  Automatic vessel tracking and manual modification. All views from CPR rotated by 360 degree and thin-slab MIP with free 3-dimensional rotation.
  The whole CTO plaque was assessed by cross-sectional views with 1-mm interval to assess the maximal luminal and vessel area of CTO, remodeling index, and semi-quantitative extent of calcification
  CT-QCA: lumen area and lesion length.
Invasive coronary angiography
  Anatomical characteristics – stump shape, side branch, collateral
  QCA
PCI
  Time for wire crossing and the end of PCI procedure
  Time for wire crossing <= 30 min
  Final procedural success (TIMI 3 flow with DS < 30%)
Notes: CCTA analysis was done with an automatic vessel tracking and manual modification,
lengths of each coronary vessel including major branches were measured.
Index of myocardial ischemia was defined as FFR ≤ 0.80

## Slide 9: % Calcification CSA (cross-sectional area) ≥ 50% suggests potentially unsuccessful PCI
Cross-sectional Calcium
0%
< 50%
> 50%
100% (full moon)
Circular
Half- and Half-moon
Crescent moon

## Slide 10: Cross-sectional calcium: semi-quantitative assessment
Central vs peripheral calc
Central sparing
Central involved
< 180 deg
≥ 180 deg
< 180 deg
≥ 180 deg
360 deg (full-moon)
None
360 deg
Applied for vessel diameter ≥2.5 mm
RCA with motion artifact may be excluded
Severe calc (CT-RECTOR wise): central calc =1,2 and/or periph calc = 2,3
≥2.5 mm
0,0
0,1
1,1
1,2
2,3
0,2
0,3

## Slide 11
1. Blunt proximal entry site
3. Occlusion length
4. Bend > 45 degree in CTO segment
5. Calcification
Bend ≤ 45 degree or bend in non-CTO segment
Total score (sum of all points) = points
Category: □ Easy (0) □ Intermediate (1) □ Difficult (2) □ Very difficult (3) □ Extremely difficult (≥4)
Peripheral calcification: maximal encircling ≥ 180⁰ and CSA ≥ 50%
Central calcification (360⁰ and CSA = 100%)
Mild calcification with encircling < 180⁰ or CSA < 50%
Tapered proximal entry site
> 45⁰
2. Proximal adjacent side branch
No side branch adjacent to proximal entry site
No calcification
Notes: CCTA analysis was done with an automatic vessel tracking and manual modification,
lengths of each coronary vessel including major branches were measured.
Index of myocardial ischemia was defined as FFR ≤ 0.80

## Slide 12
Successful guidewire crossing ≤ 30 min
A
B
C
D

## Slide 13
Fail to cross guidewire ≤ 30 min
E
F
G
H

## Slide 14
Fail to cross guidewire ≤ 30 min
E
F
G
H

## Slide 15: Clinical characteristics (643 patients)
 | All | Success to cross guidewire ≤ 30 min | Fail to cross guidewire ≤ 30 min | p-value
Patient (N) | 643 | 325 | 318 | 
Clinical risk factors |  |  |  | 
Age (year) | 62 (54 – 71) | 62 (54 – 71) | 62 (55 – 69) | 0.90
Male gender | 519 (81) | 253 (78) | 266 (84) | 0.08
Hypertension | 334 (52) | 161 (50) | 173 (54) | 0.25
Diabetes | 199 (31) | 95 (29) | 104 (33) | 0.39
Smoking | 248 (39) | 127 (39) | 121 (38) | 0.85
History of stroke | 55 (9) | 26 (8) | 29 (9) | 0.85
Prior myocardial infarction | 243 (38) | 118 (36) | 125 (39) | 0.48
Prior PCI | 138 (22) | 59 (18) | 79 (25) | 0.049
Prior bypass surgery | 22 (3) | 8 (3) | 14 (4) | 0.26
Occlusion duration ≥ 12 months or unknown | 297 (46) | 133 (41) | 164 (52) | 0.009
Laboratory and imaging tests |  |  |  | 
Hemoglobin (g/dl) | 14.0 (13.0 – 15.0) | 14.0 (13.0 – 15.0) | 14 (12.9 – 15.0) | 0.96
Creatinine (mg/dl) | 0.96 (0.82 – 1.09) | 0.93 (0.80 – 1.07) | 0.99 (0.83 – 1.10) | 0.08
Total cholesterol (mg/dl) | 157 (130 – 192) | 160 (132 – 200) | 157 (129 – 187) | 0.36
LDL cholesterol (mg/dl) | 97 (71 – 128) | 101 (74 – 131) | 92 (69 – 122) | 0.11
HDL cholesterol (mg/dl) | 42 (36 – 48) | 42 (37 – 48) | 42 (34 – 49) | 0.45
HbA1C (%) | 6.0 (5.6 – 6.9) | 5.8 (5.5 – 6.9) | 6.2 (5.8 – 6.9) | 0.07
hsCRP (mg/dl) | 0.13 (0.05 – 0.46) | 0.11 (0.05 – 0.48) | 0.15 (0.06 – 0.44) | 0.25
LV ejection fraction (%)* | 60 (55 – 66) | 60 (55 – 66) | 60 (53 – 66) | 0.74
LV ejection fraction < 40%* | 22 (5) | 11 (5) | 11 (5) | 0.99

## Slide 16: Procedural characteristics (684 vessels from 643 patients)
 | All | Success to cross guidewire ≤ 30 min | Fail to cross guidewire ≤ 30 min | p-value
Vessel (N) | 684 (100) | 350 (51) | 334 (49) | -
Radial approach | 244 (36) | 155 (44) | 89 (27) | <0.001
Guiding catheter ≥ 7Fr | 393 (58) | 188 (54) | 205 (61) | 0.051
Retrograde injection | 258 (38) | 88 (26) | 170 (51) | <0.001
Retrograde advancement of wire | 85 (12) | 6 (2) | 79 (24) | <0.001
Successful revascularization of CTO | 510 (75) | 340 (97) | 170 (51) | <0.001
Simultaneous PCI of non-CTO lesion | 192 (28) | 109 (31) | 83 (25) | 0.08
Fluoroscopy time (min) | 30 (19 – 52) | 21 (13 – 32) | 48 (29 – 69) | <0.001
Procedural time (min) | 74 (48 – 112) | 55 (37 – 78) | 98 (70 – 141) | <0.001
Contrast volume (ml) | 224 (170 – 300) | 200 (160 – 270) | 250 (190 – 345) | <0.001

## Slide 17: Angiographic characteristics
 | All | Success to cross guidewire ≤ 30 min | Fail to cross guidewire ≤ 30 min | p-value
Vessel (N) | 684 (100) | 350 (51) | 334 (49) | -
Location of CTO |  |  |  | 
LAD | 254 (37) | 142 (41) | 112 (34) | 0.06
LCX | 144 (21) | 87 (25) | 57 (17) | 0.015
RCA | 280 (41) | 118 (34) | 162 (49) | <0.001
Left main | 6 (1) | 3 (1) | 3 (1) | 0.99
Non-LAD* | 424 (62) | 205 (59) | 219 (66) | 0.07
De novo CTO | 657 (96) | 336 (96) | 321 (96) | 0.99
Multiple CTO | 104 (15) | 52 (15) | 52 (16) | 0.88
Reattempt of previously failed CTO PCI | 50 (7) | 11 (3) | 39 (12) | <0.001
Morphology |  |  |  | 
Blunt proximal entry | 258 (38) | 94 (27) | 164 (49) | <0.001
Calcification, visible within CTO segment | 250 (37) | 91 (26) | 159 (48) | <0.001
Bending > 45 degree | 338 (49) | 135 (39) | 203 (61) | <0.001
Severe vessel tortuosity (2 bendings > 70 degree or 1 bending > 90 degree) | 159 (23) | 50 (14) | 109 (33) | <0.001
Occlusion length ≥ 20 mm | 353 (52) | 129 (37) | 224 (67) | <0.001
Proximal branch | 487 (71) | 228 (65) | 259 (78) | <0.001
Distal branch | 408 (60) | 190 (54) | 218 (65) | 0.004
Functional occlusion | 32 (4.7) | 24 (6.9) | 8 (2.4) | 0.010
Proximal reference diameter (mm) | 2.85 (2.40 – 3.35) | 2.81 (2.37 – 3.35) | 2.88 (2.45 – 3.32) | 0.54
Distal reference diameter (mm) | 2.13 (1.70 – 2.55) | 2.12 (1.65 – 2.52) | 2.14 (1.74 – 2.67) | 0.36
Occlusion length (mm) | 16 (9 – 27) | 13 (7– 19) | 20 (13 – 31) | <0.001
Well-developed collateral (Rentrop=3 and Collateral connection=2) | 170 (25) | 67 (19) | 103 (31) | 0.001
Bridging collateral | 99 (15) | 46 (13) | 53 (16) | 0.37

## Slide 18: CT characteristics (1)
 | All | Success to cross guidewire ≤ 30 min | Fail to cross guidewire ≤ 30 min | p-value
Vessel (N) | 684 (100) | 350 (51) | 334 (49) | -
Vessel proximal to CTO |  |  |  | 
Angle > 90 degree from guiding to CTO segment | 317 (46) | 121 (35) | 145 (43) | 0.022
Proximal lesion with DS ≥70% | 116 (17) | 39 (11) | 77 (23) | <0.001
Length from ostium to CTO entry (mm) | 31 (17 – 47) | 32 (20 – 47) | 27 (17 – 47) | 0.39
CTO entry and exit |  |  |  | 
Blunt proximal entry | 330 (48) | 122 (35) | 208 (62) | <0.001
Blunt distal exit | 253 (37) | 97 (28) | 156 (47) | <0.001
Proximal branch | 451 (66) | 205 (59) | 246 (74) | <0.001
Distal branch | 405 (59) | 190 (54) | 215 (64) | 0.009
Tandem lesion | 16 (2) | 7 (2) | 9 (23) | 0.73
Length from CTO exit to vessel end (mm) | 85 (63 – 110) | 89 (63 – 111) | 83 (63 – 107) | 0.40
Vessel length (mm) | 144 (124 – 161) | 142 (123 – 161) | 144 (128 – 161) | 0.28
CTO plaque |  |  |  | 
Bending > 45 degree | 243 (36) | 83 (24) | 160 (48) | <0.001
Occlusion length | 15 (8 – 24) | 11 (7 – 18) | 18 (11 – 28) | <0.001
≥ 15 mm | 343 (50) | 123 (35) | 220 (66) | <0.001
Remodeling index | 1.07 (0.93 – 1.20) | 1.08 (0.96 – 1.21) | 1.05 (0.91 – 1.20) | 0.141
Positive remodeling | 298 (44) | 160 (46) | 138 (41) | 0.25
Negative remodeling | 139 (20) | 58 (17) | 81 (24) | 0.014
Proximal reference vessel area (mm2) | 8.9 (6.5 – 11.9) | 8.5 (6.4 – 11.3) | 9.0 (6.8 – 12.3) | 0.06
Distal reference vessel area (mm2) | 5.0 (3.4 – 7.3) | 5.1 (3.5 – 7.5) | 5.0 (3.2 – 7.2) | 0.32
Maximal CTO plaque area (mm2) | 10.5 (6.7 – 14.3) | 10.7 (6.6 – 13.8) | 10.0 (6.9 – 14.8) | 0.71

## Slide 19: CT characteristics (2)
 | All | Success to cross guidewire ≤ 30 min | Fail to cross guidewire ≤ 30 min | p-value
Vessel (N) | 684 (100) | 350 (51) | 334 (49) | -
Calcification of CTO plaque |  |  |  | 
Any calcification within or adjacent to CTO | 356 (52) | 154 (44) | 202 (61) | <0.001
Proximal calcification adjacent to CTO | 107 (16) | 40 (11) | 67 (20) | 0.003
Distal calcification adjacent to CTO | 113 (17) | 53 (15) | 60 (18) | 0.37
Peripheral, mild (< 180 degree or CSA < 50%) | 97 (14) | 51 (15) | 46 (14) | 0.82
Peripheral, severe (≥ 180 degree and CSA ≥ 50%) | 181 (27) | 52 (15) | 129 (39) | <0.001
Central (360 degree and CSA = 100%) | 53 (8) | 8 (2) | 45 (14) | <0.001
Visualized collateral vessel | 172 (25) | 76 (22) | 96 (29) | 0.042

## Slide 20: Development of the prediction model
 | Odds ratio for success to cross guidewire ≤ 30 min (95% CI) | Standardized beta coefficient | Point
Proximal blunt entry | 0.43 (0.30 – 0.60) | 0.85 | + 1
Proximal side branch | 0.49 (0.32 – 0.73) | 0.65 | + 1
CTO segment bending > 45 degree | 0.46 (0.31 – 0.69) | 0.75 | + 1
CTO segment length ≥ 15 mm | 0.45 (0.31 – 0.66) | 0.80 | + 1
Peripheral calcification: maximal encircling ≥ 180⁰ and CSA ≥ 50% | 0.48 (0.35 – 0.66) | 0.91 | + 1
Central calcification (CSA = 100%) |  |  | + 2
Reattempt of previously failed CTO PCI | 0.24 (0.10 – 0.51) | 0.75 | + 1
CTO duration ≥ 12month or unknown | 0.28 (0.15 – 0.51) | 0.79 | + 1
Validation was tested by leave-one-out cross-validation which is an exhaustive validation that uses each sample as validation set and the remaining observations as training set and repeats it.

## Slide 22: KCCT score vs time for guidewire crossing
0
20
40
60
80
100
120
140
160
0
1
2
3
4
5
6
7
KCCT score
Time to wire crossing (min)
8
Time to successful CTO guidewire crossing
6 78 115 124 117 61 23 4 0
N =

## Slide 23: KCCT score vs time for crossing wire <30, <60, <90, and > 90 min
Final procedural success and time to cross guidewire
0%
25%
50%
75%
100%
≤ 30 min
30 – 59 min
60 – 89 min
≥ 90 min
100%
99%
93%
83%
71%
54%
38%
31%
0%
0
1
2
3
4
5
6
7
8
6 78 122 145 156 108 55 13 1
N =
KCCT score
Successful CTO guidewire crossing ≤ 30 min
0%
25%
50%
75%
100%
0
1
2
3
4
5
6
7
8
6 78 122 145 156 108 55 13 1
N =
100%
85%
80%
59%
42%
20%
13%
7%
0%
KCCT score

## Slide 24: KCCT score for categorizing difficulty of CTO PCI
Successful guidewire crossing ≤ 30 min and procedural success according to KCCT category
0%
25%
50%
75%
100%
0
1
2
3
≥ 4
Procedural success
guidewire crossing ≤ 30 min
6 78 122 145 333
N =
100%
99%
93%
83%
58%
100%
85%
80%
59%
29%
very easy
easy
intermediate
difficult
very difficult
KCCT score =
KCCT score | Category | %wire crossing < 30min | %success
0 | Very easy | 100% | 100%
1 | Easy | 85% | 99%
2 | Intermediate | 80% | 93%
3 | Difficult | 59% | 83%
≥ 4 | Very difficult | 29% | 58%

## Slide 25
 |  |  | CTO PCI success prediction scores |  |  |  | 
 |  |  | J-CTO (Morino, JACC Intv 2011) | PROGRESS-CTO (Christopoulos, JACC Intv 2016) | CL-SCORE (Alessandrino, JACC Intv 2015) | CT-RECTOR (Opolski, JACC Intv 2015) | KCCT (This manuscript)
Anatomical predictors | CTO plaque | Proximal entry | Non-tapered stump | No tapered stump or poor cap visualization | Non-tapered stump | Non-tapered stump | Non-tapered stump
 |  | Tortuosity | Bend > 45⁰ | 2 bends >70⁰ or 1 bend >90⁰ | - | Bend > 45⁰ | Bend > 45⁰
 |  | Occlusion length | ≥ 20mm | - | ≥ 20mm | - | ≥ 15mm
 |  | Side branch | - | - | - | - | Proximal side branch
 |  | Calcification | Visualized calcification | - | Visualized calcification | Calcium CSA ≥ 50% | Calcium CSA ≥ 50%, worse if CSA =100%***
 |  | Functional occlusion | - | - | - | -** | -**
 | CTO vessel location |  | - | Worse in LCX | Worse in non-LAD | - | -
 | Collateral |  | - | Non-interventional collateral | - | - | -
Clinical predictors | Previous MI |  | - | - | Previous MI | - | -
 | CTO duration |  | - | - | - | ≥ 12 mo or unknown | ≥ 12 mo or unknown
 | Reattempt |  | Reattempt | - | - | Reattempt | Reattempt
Primary endpoint |  |  | Wire cross ≤ 30 min | Procedural success | Procedural success | Wire cross ≤ 30 min | Wire cross ≤ 30 min
Number of predicting variables |  |  | 5 | 4 | 5 | 5 | 7

## Slide 26: Comparison of KCCT score with prior published scoring systems
Successful CTO guidewire crossing ≤ 30 min
Sensitivity
Specificity
0.0
0.2
0.4
0.6
0.8
1.0
1.0
0.8
0.6
0.4
0.2
0.0
*
PROGRESS-CTO
0.635 (0.600 – 0.673)
CL-SCORE
0.702 (0.664 – 0.741)
J-CTO
0.727 (0.691 – 0.763)
CT-RECTOR
0.734 (0.698 – 0.770)
KCCT
0.787 (0.754 – 0.820)
c-statistics
* p<0.001
Final procedural success
Specificity
Sensitivity
0.0
0.2
0.4
0.6
0.8
1.0
1.0
0.8
0.6
0.4
0.2
0.0
*
PROGRESS-CTO
0.637 (0.593 – 0.682)
CL-SCORE
0.669 (0.624 – 0.714)
J-CTO
0.681 (0.638 – 0.723)
CT-RECTOR
0.717 (0.676 – 0.758)
KCCT
0.781 (0.745 – 0.818)
c-statistics
* p<0.001

## Slide 27: Comparison of KCCT score with prior published scoring systems
Cutoff | Sensitivity | Specificity | PPV | NPV
KCCT score < 4 | 71 (66 - 76) | 73 (68 – 77) | 71 (66 – 76) | 73 (68 – 77)
J-CTO score < 2 | 69 (64 – 74) | 64 (58 – 69) | 65 (59 – 69) | 68 (63 – 73)
PROGRESS-CTO score < 1 | 37 (31 - 42) | 79 (75 – 84) | 63 (56 – 70) | 57 (52 – 61)
CL-score < 3.5 | 49 (43 – 54) | 82 (78 – 86) | 72 (66 – 78) | 63 (58 – 67)
CT-RECTOR score < 3 | 65 (60 – 70) | 74 (69 – 79) | 71 (65 – 76) | 69 (64 – 74)
Cutoff | Sensitivity | Specificity | PPV | NPV
KCCT score < 4 | 80 (74 - 86) | 62 (58 – 66) | 42 (37 – 48) | 90 (87 – 93)
J-CTO score < 2 | 73 (66 – 79) | 55 (50 – 59) | 35 (31 – 41) | 86 (81 – 89)
PROGRESS-CTO score < 1 | 42 (35 - 50) | 76 (72 – 80) | 38 (31 – 45) | 79 (76 – 83)
CL-score < 3.0 | 52 (44 – 59) | 73 (69 – 77) | 40 (33 – 47) | 82 (78 – 85)
CT-RECTOR score < 3 | 71 (64 – 78) | 64 (60 – 68) | 40 (35 – 46) | 87 (83 – 90)
Successful guidewire crossing ≤ 30 min
Final procedural success

## Slide 28: Conclusion
KCCT score showed high performance for predicting guidewire crossing ≤30 min (c-statistics = 0.79) and also procedural success of CTO PCI (c-statistics = 0.78).
KCCT may enable non-invasive grading difficulty of CTO PCI.
KCCT score has a potential of improving predictive performance of prior scoring systems.